## Slide 1: tinyVP
Tiny Virtual Platform – MIPS VZ based security solution
© 2018 Leonid Yegoshin

## Slide 2: Introduction to tinyVP
Open Source hypervisor based on MIPS VZ
Security via virtualization of guests VM
Uses MIPS memory management to preserve guests VM isolation and resource assignment
Guest VM may use Microchip IDE or else
Easy learning of MIPS VZ by examples, minimal source code ̴10K lines
Expandable virtual platform for multiple cases
Static configuration in desktop build

## Slide 3: Level 1 – non paravirtualized
Pure isolating hypervizor, strict VM separation
All devices can be assigned to guests for direct registers access and DMA, root has NO drivers
Two shared devices are emulated – console UART and Interrupt Controller
No any service for guest VMs in tinyVP besides a required emulation of MIPS Architecture
Board resources allocated to guests with help of MIPS MMU + PIC32MZEF Bus Arbiter (SBU)

## Slide 4
Guest 1
Guest 2
Ethernet
CAN
Ports
And
Pins
MIPS Memory Management Unit & Microchip SBU
tinyVP kernel
TLB control
Time Service
Exception Handler
Interrupt controller
Emulator
Intr
Ctlr
Console UART Emulator
UART
tinyVP block chart

## Slide 5: Device emulation vs direct access
Device emulation
Guest
MIPS Memory Management Unit
UART
Exception Handler
Console UART emulator
Interrupt controller emulator
Direct access
Guest
MIPS Memory Management Unit
Ethernet
Interrupt controller emulator
IRQ
IRQ

## Slide 6: DMA memory protection
Guest 1
Guest 2
System Bus Arbiter
Ethernet
CAN
Access registers
Access registers
X
tinyVP kernel
Startup Board configuration

## Slide 7: Time keeping
All timing is done in 64bit values, special technique is used to extend 32bit counter:
  In case of timer interrupt miss by guest more than 32bit counter, tinyVP creates a series of timer interrupts to ensure guest accurate time. Each interrupt is presented not more than 2**31 counter value to prevent miscalculation by guest
  Time is kept in nanosecs but counter is still in clock units.
  It doesn’t prevent jitter but keeps accurate time

## Slide 8: Context switching
To minimize memory a single root IRQ stack is used with multiple short VM context frames, which keep any root VM data
tinyVP kernel
Guest 1
Guest 2
Guest 3
Frame 1
2KB
Frame 2
2KB
Frame 3
2KB
Exception/IRQ
Stack (configurable)
Simple RealTime scheduler

## Slide 9: Variable page size memory maps
Guest 2
Guest 1
tinyVP kernel
Static configuration allows to use a full advantage of MIPS variable page sizes – easy fit a couple of VM maps into small array of 16 TLB elements: big pages cover main memory, small pages do a fine-tune device register blocks
PTEs
PTEs
PTEs
PTEs
Device region
Memory region
Memory region
Memory region
PTEs
PTEs
PTEs
PTEs
PTEs
PTEs root
Variable Page Tables Trees

## Slide 10: Desktop build chart
Phase 1
Memory Map creation
Config
file
Platform files
Device library
Phase 2A
Configuration arrays creation
tinyVP source
Phase 2B
Binary build by toolchain
Guest 1
ELF
Guest 2 binary img
tinyVP kernel
tVP
G1
G2
.c .h
.map
a.out
a.merged.srec
Flash

## Slide 11: Flexible configuration and setup
config.file - main system configuration
platforms/* - platform specific files:
  Python lib script for SoC specific configuration
  Assembler file with SoC specific functions like board unlock, flash ECC setup etc
boards/* - board-specific files sets:
  Memory/flash/tinyVP addrs, PMD regs basic setup
  Board EFUSE setup module
  Board-specific assembler - pin routing, power mgmt setup, LED sequencer etc
device.lib - device decriptions library

## Slide 12: Key benefits
Smallest memory footprint and source code
Non-paravirtualized, no drivers in kernel need, direct access to device regs by guests
Protection against malicious DMA by SBA
Static configuration allows variable page sizes which efficiently fits low number of TLBs
Allows using Microchip IDE for guest development, example – MyNewT RTOS
Bare-metal guests may run w/out code change (some limitations do exist)

## Slide 13: Some key benchmarks data
Basic hypervisor call 69-75 clocks
Force context switch 336-343 clocks
Emulation of register access 208 clocks
IRQ injection 173 clocks
Device IRQ round trip via guest 512-580 clock (2nd IRQ happens before guest finishes 1st)
Memory footprint (no debug) 36-42 KB
Measurement is in CPU clock cycles, each clock is 2 instructions, difference is toolchain optimization
(Times may slightly change in future development)

## Slide 14: Level 2 – root multithreading
Target – protected run of communication state machines in separate virtual address space, w/out IRQ/Exception/Device service hazzle, just message exchange
VirtIO as a way for message exchange between various state machines and guests
It is a departure from “no service in root kernel” but it simplifies development of communication stack
(In development…)

## Slide 15: Typical use case – secure flash
Flash control runs in background with main application
After collecting and verification of new flash image it writes it into flash
Next reboot gives an updated main app
Main application doesn’t care about flash memory, in fact it has no write access to it.

## Slide 16: Typical use case – secure execution
Guest VM is designed without virtualization, on bare-metal IoT board
But tinyVP runs it as a guest VM and restricts guest access to some critical communication devices
In any point a central control can inquire the stability of guest VM via comm device and can stop or restart guest VM

## Slide 17: Typical use case – communication stack isolation
  (Level 2 is needed)
Communication stack state machines are put into separate threads with full memory protection from guests or other SM
It provides secure kind of scenario then some communication should be protected agains guest VM intrusion, like drone communication with air control in open-source drone software